## Slide 1
Lecture 01
Computer System Fundamentals
Basic Elements · Registers · Instruction Cycle · Interrupts
SENG 21213 · Computer Architecture & Operating Systems
1

## Slide 2
Learning Objectives
SENG 21213 · Computer Architecture & Operating Systems
2
By the end of this lecture you should be able to:
1. Identify the four basic computer components and describe the role of each
2. Explain the function of MAR, MBR, I/OAR and I/OBR using register-transfer notation
3. Trace a program execution step-by-step through the fetch-execute cycle
4. Classify instructions into four categories: processor-memory, processor-I/O, data processing, control
5. Describe the complete 9-step interrupt processing sequence from IRQ to ISR return
6. Compare sequential and nested multiple-interrupt strategies with their trade-offs

## Slide 3
Section 1
The Four Basic Elements
3

## Slide 4
Top-Level View of Computer Components
SENG 21213 · Computer Architecture & Operating Systems
4
CPU, Main Memory, I/O Modules, and System Bus — the four building blocks of every computer system (Stallings Fig. 1.1)

## Slide 5
The Four Basic Elements
SENG 21213 · Computer Architecture & Operating Systems
5
Component | Function | Key Characteristics
Processor (CPU) | Controls operations; performs data processing | Contains ALU and CU; executes instruction cycle; single or multi-core
Main Memory | Stores instructions and data currently in use | Volatile; byte/word addressable; also called RAM or primary memory
I/O Modules | Transfer data between computer and external devices | Contains data buffers; examples: disk controller, NIC, keyboard controller
System Bus | Communication pathway between all components | Carries address, data, and control signals; shared resource with arbitration

## Slide 6
Section 2
CPU Registers & Instruction Cycle
6

## Slide 7
Four Key CPU Registers
SENG 21213 · Computer Architecture & Operating Systems
7
Register | Full Name | Role
MAR | Memory Address Register | Holds address of next memory read/write — CPU sets this before any memory access
MBR | Memory Buffer Register | Holds data just read from or about to be written to memory — acts as a buffer
I/OAR | I/O Address Register | Specifies which I/O device (port address) the current transfer targets
I/OBR | I/O Buffer Register | Holds data exchanged between CPU and the selected I/O module

## Slide 8
The Fetch-Execute Cycle
SENG 21213 · Computer Architecture & Operating Systems
8
Two-phase instruction cycle: FETCH (load next instruction) → EXECUTE (carry out the operation) — repeats until HALT (Stallings Fig. 1.2)

## Slide 9
Fetch Stage — Five Micro-Operations
SENG 21213 · Computer Architecture & Operating Systems
9
MAR ← PC (copy Program Counter to Memory Address Register)
MBR ← Memory[MAR] (read instruction word from memory into MBR)
IR ← MBR (copy instruction to Instruction Register for decoding)
PC ← PC + 1 (advance Program Counter to next instruction)
Decode: Control Unit reads opcode from IR[15:12] to determine instruction type

## Slide 10
Instruction Format — Opcode + Address
SENG 21213 · Computer Architecture & Operating Systems
10
4-bit opcode (one hex digit) | 12-bit address (three hex digits) — 1940 hex = opcode 1 (LOAD), address 940 (Stallings Fig. 1.4)

## Slide 11
Four Instruction Categories
SENG 21213 · Computer Architecture & Operating Systems
11
Category | Description | Example
Processor-Memory | Data transferred between CPU and main memory | LOAD AC from Memory[940]; STORE AC to Memory[941]
Processor-I/O | Data transferred between CPU and I/O module | READ from keyboard port; WRITE to serial port
Data Processing | ALU performs arithmetic or logic on registers | ADD AC with Memory[941]; AND AC with bitmask value
Control | Instruction alters the Program Counter — branch/jump | JMP 182 (unconditional); BEQ label (conditional)

## Slide 12
Complete Execution Trace — Stallings Fig. 1.3
SENG 21213 · Computer Architecture & Operating Systems
12
Step-by-step trace: LOAD 940 → ADD 941 → STORE 941 showing PC, MAR, MBR, IR, AC at each step

## Slide 13
Common Mistake — PC Increment Timing
SENG 21213 · Computer Architecture & Operating Systems
13
⚠ PC Increments During FETCH, Not After Execute
The PC is incremented in step 4 of the FETCH stage (PC ← PC + 1)
By the time EXECUTE begins, the PC already points to the NEXT instruction
This enables the CPU to begin fetching the next instruction during execute (pipelining)
Exam trap: "what does PC contain during execute of instruction at address 300?" → Answer: 301

## Slide 14
Section 3
Interrupts
14

## Slide 15
Why Interrupts? — The Motivation
SENG 21213 · Computer Architecture & Operating Systems
15
Without interrupts: CPU must POLL devices in a tight loop (Programmed I/O)
A 1 GHz CPU doing 1 I/O operation per 4 ms wastes 4,000,000 cycles spinning
Interrupts allow the CPU to execute useful work while I/O proceeds in background
When device finishes: it asserts an IRQ signal → CPU runs a short ISR → resumes
Result: CPU utilisation improves from ~30% to >90% on I/O-bound workloads

## Slide 16
Extended Instruction Cycle with Interrupt Check
SENG 21213 · Computer Architecture & Operating Systems
16
After each Execute stage, the CPU checks for pending interrupts before fetching the next instruction (Stallings Fig. 1.8)

## Slide 17
9-Step Interrupt Processing Sequence
SENG 21213 · Computer Architecture & Operating Systems
17
Step | Who | Action
1 | Device | Asserts IRQ signal on interrupt bus to CPU
2 | CPU | Finishes current instruction completely — no mid-instruction interrupts
3 | CPU → Device | CPU asserts interrupt acknowledge; device removes IRQ
4 | CPU | Saves PSW + PC onto kernel control stack (minimum context)
5 | CPU | Loads PC from Interrupt Vector Table entry for this interrupt type
6 | ISR | Saves ALL general registers (EAX–EDI, EBP) — ISR will use them
7 | ISR | Services the interrupt: reads device status, transfers data
8 | ISR | Restores all saved general registers (reverse of step 6)
9 | ISR | Restores PSW + PC from stack; CPU resumes interrupted program

## Slide 18
Multiple Interrupts — Two Strategies
SENG 21213 · Computer Architecture & Operating Systems
18
Sequential (Disable Interrupts)
CPU sets interrupt-disable flag during ISR
New IRQs held pending until re-enable
ISRs run to completion — no nesting
Simple; no stack overflow risk
Problem: slow ISRs delay time-critical events
Nested (Priority-Based)
ISRs run at a priority level
Higher-priority IRQ interrupts lower ISR
Time-critical events handled immediately
Requires nested stack of saved contexts
Problem: stack overflow if too many levels

## Slide 19
Nested Interrupt Processing
SENG 21213 · Computer Architecture & Operating Systems
19
Multiple interrupt sources with different priorities — higher priority ISR preempts lower priority ISR mid-execution (Stallings Fig. 1.12)

## Slide 20
Practice Exercise
SENG 21213 · Computer Architecture & Operating Systems
20
✎ Exercise 1.1 — Instruction Trace [10 marks]
A processor executes: (1) LOAD AC from Memory[940], (2) ADD Memory[941], (3) STORE to Memory[941]
(a) [4] Draw the complete 6-step execution trace showing PC, MAR, MBR, IR, AC at each step
(b) [3] Write the three 16-bit instruction words as 4-digit hex (opcode 1=LOAD, 5=ADD, 2=STORE)
(c) [3] At what point during the trace is the PC updated to point to instruction 2? Explain why

## Slide 21
Key Takeaways
Computer System Fundamentals
Four basic elements: Processor, Main Memory, I/O Modules, System Bus
MAR holds address; MBR holds data — every memory access uses both
Fetch: MAR←PC; MBR←Memory[MAR]; IR←MBR; PC←PC+1; then decode
Four instruction categories: processor-memory, I/O, data processing, control
9-step interrupt: IRQ → finish instruction → acknowledge → save context → ISR → restore
Sequential vs. nested interrupts: simplicity vs. responsiveness trade-off
21