## Slide 1
Lecture 03
Data Representation & Combinational Circuits
Number Systems · 2's Complement · IEEE 754 · Boolean Algebra · Logic Gates
SENG 21213 · Computer Architecture & Operating Systems
1

## Slide 2
Learning Objectives
SENG 21213 · Computer Architecture & Operating Systems
2
By the end of this lecture you should be able to:
1. Convert numbers between binary, decimal, octal, and hexadecimal using positional notation
2. Represent signed integers in sign-magnitude, 1's complement, and 2's complement and detect overflow
3. Encode and decode IEEE 754 single-precision floating-point numbers
4. Apply all Boolean algebra laws including De Morgan's theorems to simplify logic expressions
5. Design and analyse half adder, full adder, MUX, and decoder circuits

## Slide 3
Section 1
Number Systems & Signed Integers
3

## Slide 4
Number System Conversions
SENG 21213 · Computer Architecture & Operating Systems
4
Binary | Octal | Decimal | Hex | Notes
00000000 | 000 | 0 | 00 | Zero
00001010 | 012 | 10 | 0A | Ten
00001111 | 017 | 15 | 0F | Max nibble (4-bit max)
01111111 | 177 | 127 | 7F | Max positive 8-bit signed
10000000 | 200 | 128 | 80 | Min unsigned = most-negative signed
11111111 | 377 | 255 | FF | Max unsigned 8-bit

## Slide 5
Signed Integer Representations (8-bit, showing ±7)
SENG 21213 · Computer Architecture & Operating Systems
5
Scheme | Positive +7 | Negative −7 | Range (n-bit) | Zeros
Sign-magnitude | 0000 0111 | 1000 0111 | −127 to +127 | Two: +0 and −0
1's complement | 0000 0111 | 1111 1000 | −127 to +127 | Two: 00..0 and 11..1
2's complement | 0000 0111 | 1111 1001 | −128 to +127 | One: 00..0 only

## Slide 6
2's Complement Conversion
SENG 21213 · Computer Architecture & Operating Systems
6
★ Two's Complement — Procedure and Verification
To negate: Step 1: Write positive value (e.g. +7 = 0000 0111)
Step 2: Invert ALL bits (NOT): 1111 1000
Step 3: Add 1: 1111 1001 = −7 ✓
Verify: 1111 1001 + 0000 0111 = 1 0000 0000 → carry out; discard it → 0000 0000 = 0 ✓
Special case: −128 in 8-bit has no positive counterpart (+128 overflows). Negating −128 → −128 again.
Overflow rule: Positive + Positive = Negative, or Negative + Negative = Positive → signed overflow

## Slide 7
Section 2
IEEE 754 Floating-Point
7

## Slide 8
IEEE 754 Formats
SENG 21213 · Computer Architecture & Operating Systems
8
Format | Sign | Exponent | Mantissa | Bias | Value Range
Single (32-bit) | 1 bit | 8 bits | 23 bits | 127 | ±1.18×10⁻³⁸ to ±3.4×10³⁸
Double (64-bit) | 1 bit | 11 bits | 52 bits | 1023 | ±2.2×10⁻³⁰⁸ to ±1.8×10³⁰⁸

## Slide 9
IEEE 754 Encoding
SENG 21213 · Computer Architecture & Operating Systems
9
★ Encoding 6.5 in Single-Precision
Step 1: Convert 6.5 to binary: 110.1₂
Step 2: Normalise: 1.101 × 2² (move point left 2 places)
Step 3: Sign bit = 0 (positive)
Step 4: Biased exponent = 2 + 127 = 129 = 1000 0001₂
Step 5: Mantissa = fractional part of 1.101 → 101 padded to 23 bits: 10100000000000000000000
Result: 0 10000001 10100000000000000000000 = 0x40D00000

## Slide 10
Section 3
Boolean Algebra & Logic Gates
10

## Slide 11
Basic Gates and Operations
SENG 21213 · Computer Architecture & Operating Systems
11
Gate | Expression | A=0,B=0 | A=0,B=1 | A=1,B=0 | A=1,B=1 | Key Property
AND | Y=A·B | 0 | 0 | 0 | 1 | ALL inputs must be 1
OR | Y=A+B | 0 | 1 | 1 | 1 | ANY input = 1 → output 1
NOT | Y=A' | — | 1 (A=0) | 0 (A=1) | — | Inversion (complement)
NAND | Y=(A·B)' | 1 | 1 | 1 | 0 | Universal gate — builds any circuit
XOR | Y=A⊕B | 0 | 1 | 1 | 0 | Output 1 iff inputs DIFFER

## Slide 12
Key Boolean Algebra Laws
SENG 21213 · Computer Architecture & Operating Systems
12
Law | AND form | OR form
Identity | A · 1 = A | A + 0 = A
Null | A · 0 = 0 | A + 1 = 1
Idempotent | A · A = A | A + A = A
Complement | A · A' = 0 | A + A' = 1
Double Negation | (A')'= A | —
Distributive | A·(B+C) = A·B+A·C | A+(B·C) = (A+B)·(A+C)
De Morgan | (A·B)' = A'+B' | (A+B)' = A'·B'
Absorption | A·(A+B) = A | A+(A·B) = A

## Slide 13
Section 4
Combinational Circuits
13

## Slide 14
Full Adder Truth Table
SENG 21213 · Computer Architecture & Operating Systems
14
A | B | Cin | Sum | Cout
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1

## Slide 15
Full Adder Equations
SENG 21213 · Computer Architecture & Operating Systems
15
★ Full Adder — Boolean Expressions
Sum = A ⊕ B ⊕ Cin (three-way XOR)
Cout = A·B + A·Cin + B·Cin = A·B + Cin·(A⊕B)
Built from 2 half adders: HA1(A,B)→S1,C1; HA2(S1,Cin)→Sum,C2; Cout = C1+C2
Ripple-carry adder: chain N full adders — carry ripples from bit 0 to bit N−1
Delay = N × gate delay — 32-bit ripple adder ≈ 32 × 2ns = 64ns (at 1ns/gate)
Carry-lookahead adder computes all carries simultaneously — reduces to O(log N) delay

## Slide 16
Practice Exercise
SENG 21213 · Computer Architecture & Operating Systems
16
✎ Exercise 3.1 — Number Systems & Boolean Algebra [10 marks]
(a) [3] Convert 01101110₂ to: (i) decimal, (ii) hex, (iii) octal. Show positional notation.
(b) [3] Express −75 in 8-bit 2's complement. Verify by adding to +75. Show each step.
(c) [4] Simplify F = A'BC + ABC + A'B'C + AB'C to minimal SOP form. State each law used.

## Slide 17
Key Takeaways
Data Representation & Combinational Circuits
Positional notation: binary ↔ hex (4 bits each); binary ↔ octal (3 bits each)
2's complement: invert + 1; single zero; standard CPU arithmetic; overflow = sign change
IEEE 754: sign | biased exponent (exp + bias) | mantissa (fractional part of 1.xxx)
De Morgan: (A·B)' = A'+B' and (A+B)' = A'·B' — push negation through gates
Full adder: Sum = A⊕B⊕Cin; Cout = AB + Cin(A⊕B) — chain N for n-bit adder
NAND and NOR are universal: any Boolean function can be built from either gate alone
17