## Slide 1
Lecture 04
Sequential Circuits & Computer Architectures
Flip-Flops · Registers · FSMs · CISC vs RISC · Von Neumann vs Harvard
SENG 21213 · Computer Architecture & Operating Systems
1

## Slide 2
Learning Objectives
SENG 21213 · Computer Architecture & Operating Systems
2
By the end of this lecture you should be able to:
1. Describe SR latch, D flip-flop, and JK flip-flop behaviour from their characteristic tables
2. Design synchronous registers, shift registers, and binary counters using T flip-flops
3. Follow the 7-step FSM design procedure and distinguish Moore from Mealy machines
4. Compare CISC and RISC architectures on 10 key attributes
5. Explain Von Neumann vs. Harvard architectures and how modern CPUs use Modified Harvard

## Slide 3
Section 1
Flip-Flops and Sequential Logic
3

## Slide 4
D and JK Flip-Flop Characteristic Tables
SENG 21213 · Computer Architecture & Operating Systems
4
Flip-Flop | Inputs | Q (next) | Operation
D (Data) | CLK↑, D=0 | 0 | Captures D on rising clock edge
D (Data) | CLK↑, D=1 | 1 | Q = D always on clock edge — no forbidden state
JK | J=0, K=0 | Q (hold) | Hold — no change
JK | J=1, K=0 | 1 | Set — Q becomes 1
JK | J=0, K=1 | 0 | Reset — Q becomes 0
JK | J=1, K=1 | Q' | Toggle — eliminates SR forbidden state

## Slide 5
D Flip-Flop Timing
SENG 21213 · Computer Architecture & Operating Systems
5
★ Timing Constraints — Setup, Hold, Propagation
Setup time (t_su): D must be stable for t_su BEFORE the clock edge
Hold time (t_h): D must remain stable for t_h AFTER the clock edge
Propagation delay (t_pd): Q changes within t_pd after the clock edge
Max frequency: f_max = 1 / (t_pd + t_su + routing_delay)
Violation of setup/hold → metastability: output oscillates between 0 and 1 unpredictably
Example: t_pd=3ns, t_su=1ns → f_max = 1/(3+1) = 250 MHz maximum

## Slide 6
Register Types and Uses
SENG 21213 · Computer Architecture & Operating Systems
6
Type | Structure | Operation | Use Case
Parallel n-bit | n D flip-flops, shared clock | All n bits load simultaneously on clock edge | CPU general-purpose registers, ALU operand buffering
SIPO (shift register) | n flip-flops chained; D_n = Q_{n-1} | One bit in per cycle; after n cycles all bits present | Serial→parallel conversion: UART receive
PISO (shift register) | Load logic + chain | Load n bits in one cycle; shift out serially | Parallel→serial: UART transmit
Bidirectional | MUX on D selects left/right shift | Shifts ±1 per cycle | Arithmetic shift ×2 or ÷2

## Slide 7
Section 2
Finite State Machines
7

## Slide 8
Moore vs. Mealy Machines
SENG 21213 · Computer Architecture & Operating Systems
8
Moore Machine
Output depends on CURRENT STATE only
Output changes only on clock edge (state change)
Outputs are glitch-free — stable until next clock
Typically requires MORE states for same function
Output written INSIDE state circles in diagram
Example: traffic light controller, vending machine
Mealy Machine
Output depends on STATE + CURRENT INPUT
Output can change asynchronously with input
May produce momentary glitches on input changes
Typically requires FEWER states for same function
Output written ON TRANSITION arrows in diagram
Example: data parser, handshaking protocol

## Slide 9
FSM Design Procedure
SENG 21213 · Computer Architecture & Operating Systems
9
★ 7-Step FSM Design Process
Step 1: Define what the system must REMEMBER — these become the states
Step 2: Identify all inputs (cause transitions) and outputs (produced per state/transition)
Step 3: Draw State Transition Diagram (STD): circles=states, arrows=transitions labelled input/output
Step 4: Encode states as binary: n flip-flops needed for up to 2ⁿ states
Step 5: Build state transition table — (current state, input) → (next state, output)
Step 6: Derive next-state Boolean equations using algebra or Karnaugh maps
Step 7: Implement with flip-flops + combinational logic (gates or MUXes)

## Slide 10
Section 3
Computer Architecture — CISC vs RISC
10

## Slide 11
CISC vs. RISC — 10 Key Attributes
SENG 21213 · Computer Architecture & Operating Systems
11
Attribute | CISC | RISC
Instruction count | Fewer (complex ops in one instr) | More (simple ops, more instrs needed)
Instruction length | Variable (x86: 1–15 bytes) | Fixed (MIPS/ARM: exactly 4 bytes)
Addressing modes | Many (10–20+) | Few (3–5); load/store only for memory
Register count | Few special (EAX,EBX,ECX,EDX) | Many general-purpose (32 on MIPS)
Memory access | Many instrs can read/write memory | ONLY LW and SW instructions access memory
CPI | Variable, often > 1 | Close to 1 (designed for pipelining)
Control unit | Microprogrammed (flexible, slow) | Hardwired (fast, rigid)
Pipeline support | Hard (variable length instrs) | Designed for pipelining from start
Compiler burden | Low (hardware does complex work) | High (compiler manages registers)
Examples | x86, x86-64, VAX | MIPS, ARM, RISC-V, PowerPC, SPARC

## Slide 12
Von Neumann vs Harvard
SENG 21213 · Computer Architecture & Operating Systems
12
★ Architectural Memory Organisation
Von Neumann: ONE shared memory space for both instructions and data; ONE bus
Bottleneck: instruction fetch and data access COMPETE for the same bus — von Neumann bottleneck
Harvard: SEPARATE instruction and data memories with SEPARATE buses — no contention
CPU can fetch next instruction while reading/writing data — two accesses in parallel
Modified Harvard (modern CPUs): physically one main memory; separate L1-I (instruction) and L1-D (data) caches at top level
Your OS kernel: Flash for instructions + RAM for data → real Modified Harvard

## Slide 13
Practice Exercise
SENG 21213 · Computer Architecture & Operating Systems
13
✎ Exercise 4.1 — Flip-Flop Timing [12 marks]
(a) [4] D flip-flop: t_pd=3ns, t_su=1ns, t_h=0.5ns. Combinational logic between FFs = 5ns delay. What is f_max? Draw the critical path.
(b) [4] 4-bit synchronous counter using T flip-flops. Write T₃, T₂, T₁, T₀ Boolean expressions. Draw timing diagram for 10 clock cycles from 0000.
(c) [4] Design a Moore FSM that detects the sequence "101" in a serial bit stream. Show STD and state transition table.

## Slide 14
Key Takeaways
Sequential Circuits & Computer Architectures
D flip-flop captures D on clock edge — building block of all registers and state machines
JK flip-flop: J=K=1 toggles — eliminates forbidden state of SR latch
FSM design: state = what to remember; 7 steps from requirements to implementation
Moore: output from state only; Mealy: output from state + input; Mealy uses fewer states
RISC: fixed-length, load/store, many registers, hardwired CU — designed for pipelining
CISC: variable-length, memory operands, microprogrammed — code density but hard to pipeline
14