## Slide 1
Lecture 05
Processor Architecture & ISA
ALU · Control Unit · ISA · Addressing Modes · CPU Performance · Amdahl's Law
SENG 21213 · Computer Architecture & Operating Systems
1

## Slide 2
Learning Objectives
SENG 21213 · Computer Architecture & Operating Systems
2
By the end of this lecture you should be able to:
1. Describe ALU operations and the status flags produced by each operation group
2. Compare hardwired and microprogrammed control units on speed, flexibility, and use case
3. Explain MIPS R-type, I-type, and J-type instruction formats with field widths
4. Apply all 8 addressing modes to resolve effective addresses
5. Calculate CPU execution time using T = N × CPI × T_clock
6. Apply Amdahl's Law to predict parallel speedup and derive required parallelisable fraction

## Slide 3
Section 1
ALU and Control Unit
3

## Slide 4
ALU Operations and Status Flags
SENG 21213 · Computer Architecture & Operating Systems
4
Operation Group | Operations | Flags Produced
Integer Arithmetic | ADD, ADDC, SUB, SUBB, MUL, DIV, INC, DEC, NEG | Z (result=0), N (MSB=1), C (carry/borrow), V (signed overflow)
Logical | AND, OR, NOT, XOR, NAND, NOR | Z (result=0), N (MSB=1)
Shift / Rotate | SHL, SHR, SAR (arithmetic), ROL, ROR | C (last bit shifted out), Z (result=0)
Compare | CMP (SUB; discard), TEST (AND; discard) | All flags — flags ARE the purpose of these instructions
Bit Manipulation | BIT, SET, CLEAR, FLIP (test/set/clear/toggle a bit) | Z (tested bit state)

## Slide 5
Control Unit — Hardwired vs. Microprogrammed
SENG 21213 · Computer Architecture & Operating Systems
5
Hardwired CU
Combinational logic decodes opcode → control signals in one step
Fast — one gate delay per control signal
Rigid — changing ISA requires hardware redesign
Simple for RISC (small ISA); grows exponentially for CISC
Examples: all modern RISC CPUs (MIPS, ARM, RISC-V)
Microprogrammed CU
Each machine instruction → sequence of microinstructions in Control Store ROM
Slower — extra memory read per microinstruction
Flexible — new instructions = update firmware
Manages CISC complexity by decomposing into simple micro-ops
Examples: x86 CPUs (Intel microcode, updated for Spectre)

## Slide 6
Section 2
ISA — Instruction Formats & Addressing
6

## Slide 7
MIPS Instruction Formats
SENG 21213 · Computer Architecture & Operating Systems
7
★ Three Fixed-Width 32-bit Formats
R-type (Register): OP[6] | rs[5] | rt[5] | rd[5] | shamt[5] | funct[6] → 32 bits
→ Used for: ADD, SUB, AND, OR, SLT — all three operands are registers
I-type (Immediate): OP[6] | rs[5] | rt[5] | immediate[16] → 32 bits
→ Used for: ADDI, LW (load), SW (store), BEQ, BNE — constant or memory address
J-type (Jump): OP[6] | target[26] → 32 bits
→ Used for: J (jump), JAL (jump and link for subroutine calls)
Fixed width: every instruction is exactly 4 bytes — enables clean, efficient pipelining

## Slide 8
Eight Addressing Modes
SENG 21213 · Computer Architecture & Operating Systems
8
Mode | x86 Syntax | Effective Address (EA) | Typical Use
Immediate | MOV EAX, 42 | EA = none; operand = 42 | Loading constants
Register | ADD EAX, EBX | EA = none; operand = EBX content | Fast local variable ops
Direct | MOV EAX, [0x1000] | EA = 0x1000 | Global/static variable
Register Indirect | MOV EAX, [EBX] | EA = EBX | Pointer dereference (*ptr)
Register + Displacement | MOV EAX, [EBX+8] | EA = EBX + 8 | Struct field access
Base + Index | MOV EAX, [EBX+ESI] | EA = EBX + ESI | Array traversal
Base+Index+Disp | MOV EAX, [EBX+ESI*4+8] | EA = EBX + ESI×4 + 8 | Array-of-structs
PC-Relative | JMP label | EA = PC + offset | Branches, PIC code

## Slide 9
Section 3
CPU Performance & Amdahl's Law
9

## Slide 10
CPU Performance Equation
SENG 21213 · Computer Architecture & Operating Systems
10
★ T_cpu = N × CPI × T_clock
N = Instruction count (depends on program and ISA — compiler reduces N)
CPI = Cycles Per Instruction (average over all instruction types)
T_clock = 1/f — reduce by increasing clock frequency
Mixed CPI: CPI_avg = Σ(fraction_i × CPI_i) — weighted average across instruction types
Example: 60% INT (CPI=1) + 20% FP (CPI=4) + 20% MEM (CPI=2) → CPI_avg = 0.6+0.8+0.4 = 1.8
Cannot optimise all three independently — improving one often degrades another (compiler trade-offs)

## Slide 11
Amdahl's Law
SENG 21213 · Computer Architecture & Operating Systems
11
★ Maximum Speedup from Parallelism
Speedup = 1 / [s + (1−s)/p]
s = serial fraction (0 ≤ s ≤ 1); p = number of processors
Maximum speedup (p → ∞): Speedup_max = 1/s
Example: 20% serial (s=0.2) → max speedup = 1/0.2 = 5× regardless of CPU count
4 CPUs with s=0.2: Speedup = 1/(0.2 + 0.8/4) = 1/0.4 = 2.5×
Implication: Reduce the serial fraction, not just add cores. 99% parallel → max 100× speedup.

## Slide 12
Amdahl's Law — Speedup Table
SENG 21213 · Computer Architecture & Operating Systems
12
Serial Fraction (s) | Max Speedup (∞ CPUs) | 4 CPUs | 16 CPUs | 64 CPUs
50% | 2× | 1.60× | 1.88× | 1.97×
20% | 5× | 2.50× | 3.81× | 4.71×
10% | 10× | 3.08× | 6.40× | 8.64×
5% | 20× | 3.48× | 9.75× | 15.6×
1% | 100× | 3.88× | 14.8× | 39.4×

## Slide 13
Practice Exercise
SENG 21213 · Computer Architecture & Operating Systems
13
✎ Exercise 5.1 — CPU Performance [12 marks]
CPU at 3.2 GHz, 4×10⁹ instructions: 50% INT(CPI=1), 25% MEM(CPI=3), 25% FP(CPI=4)
(a) [4] Calculate CPI_avg and total execution time.
(b) [4] New FPU reduces FP CPI from 4 to 1.5. New CPI_avg? New execution time? Speedup?
(c) [4] Clock raised to 4.0 GHz but CPI increases from 1.875 to 2.2 (pipeline stalls). Which design is faster? Show all working.

## Slide 14
Key Takeaways
Processor Architecture & ISA
ALU: five operation groups; flags C (carry), Z (zero), N (negative), V (overflow)
Hardwired CU = fast, rigid (RISC); Microprogrammed = flexible, slower (CISC/x86)
MIPS: R/I/J-type fixed 32-bit; load/store ISA — all ALU ops use registers only
8 addressing modes: immediate, register, direct, indirect, displaced, indexed, scaled, PC-relative
T_cpu = N × CPI × T_clock — three independent levers; optimising one affects others
Amdahl: Speedup_max = 1/s — serial fraction is the fundamental parallelism bottleneck
14