## Slide 1
Lecture 06
Pipelining, Branch Prediction & Parallelism
5-Stage Pipeline · Hazards · Branch Prediction · Flynn's Taxonomy · ILP
SENG 21213 · Computer Architecture & Operating Systems
1

## Slide 2
Learning Objectives
SENG 21213 · Computer Architecture & Operating Systems
2
By the end of this lecture you should be able to:
1. Describe the operation of each stage in the 5-stage RISC pipeline
2. Calculate pipeline speedup and explain the impact of hazards on ideal CPI
3. Identify structural, data (RAW), and control hazards and describe resolution techniques
4. Trace 2-bit saturating counter branch predictor state transitions and count mispredictions
5. Classify processor organisations using Flynn's taxonomy (SISD, SIMD, MISD, MIMD)
6. Describe superscalar, OOO execution, VLIW, and SMT techniques for exploiting ILP

## Slide 3
Section 1
The 5-Stage Pipeline
3

## Slide 4
Five Pipeline Stages
SENG 21213 · Computer Architecture & Operating Systems
4
Stage | Name | Hardware Used | Operation
IF | Instruction Fetch | I-Cache, PC reg | MAR←PC; IR←I-Cache[MAR]; PC←PC+4
ID | Instruction Decode | Control unit, register file | Decode opcode; read rs,rt; sign-extend immediate
EX | Execute | ALU, forwarding unit | ALU computes result/address/branch target; flags set
MEM | Memory Access | D-Cache | Load: read D-Cache; Store: write D-Cache; others: pass-through
WB | Write Back | Register file | Write ALU result or loaded data to destination register rd

## Slide 5
Pipeline Performance
SENG 21213 · Computer Architecture & Operating Systems
5
★ Throughput and Speedup
Ideal CPI = 1 — one instruction completes per clock cycle in steady state
Start-up latency: first result after k cycles (k = number of stages)
N instructions on k-stage pipeline: k + (N−1) cycles (≈ N for large N)
Theoretical speedup over sequential = k (k = 5 for RISC)
Actual speedup < k due to hazards, branch mispredictions, cache misses
Example: 100 instructions, 5-stage: 5+99=104 cycles vs. 500 sequential → 4.8× speedup

## Slide 6
Section 2
Pipeline Hazards
6

## Slide 7
Three Types of Pipeline Hazards
SENG 21213 · Computer Architecture & Operating Systems
7
Hazard Type | Cause | Detection | Resolution Strategy
Structural | Two instructions need the SAME hardware at the SAME time | Check if resources are single-ported | Split L1 into I-cache and D-cache — separate ports eliminate IF/MEM conflict
Data (RAW) | Instruction needs result not yet written (Read After Write) | Compare rd of recent instrs with rs/rt of current instr | Forwarding: route EX/MEM result back to ALU input; or stall (insert NOPs)
Control (Branch) | Branch changes PC — wrong instructions may already be fetched | Detected when branch resolves in EX or MEM stage | Predict, delay slot, flush on mispredict — see next slides

## Slide 8
Data Hazard — Forwarding
SENG 21213 · Computer Architecture & Operating Systems
8
★ RAW Hazard Resolution
Without forwarding: ADD R1,R2,R3 followed by SUB R4,R1,R5 → 2-cycle stall (R1 not in regfile yet)
With forwarding: route EX stage result directly to ALU input of next instruction
EX→EX forwarding: eliminates 2-cycle stall for most ALU→ALU dependencies
MEM→EX forwarding: eliminates 1-cycle stall for ALU→memory→ALU dependencies
Load-use hazard: LW R1,0(R2) followed immediately by ADD R3,R1,R4 — still 1-cycle stall even with forwarding (data not available until end of MEM stage)
Compiler can reorder instructions to fill the load-use slot with independent work

## Slide 9
Branch Prediction Strategies
SENG 21213 · Computer Architecture & Operating Systems
9
Strategy | Mechanism | Penalty on Mispredict | Accuracy
Always flush | Stall until branch resolved; fetch correct path | 2–3 cycles every branch | 100% — but very slow
Predict not-taken | Continue sequential fetch; flush if branch taken | 2–3 cycles only if taken | 40–60%
Delayed branch (MIPS) | Fill branch delay slot with guaranteed-useful instr | 0 cycles | 100% — compiler responsibility
2-bit saturating counter | 4-state predictor; stable under repeated patterns (loops) | 2–3 cycles on mispredict | ~90%
Tournament predictor (modern) | Meta-predictor selects between global+local predictors | 2–15 cycles on mispredict | ~97–99%

## Slide 10
2-Bit Saturating Counter — State Transitions
SENG 21213 · Computer Architecture & Operating Systems
10
State | Prediction | If Branch TAKEN | If Branch NOT TAKEN
Strongly Taken (11) | Taken | Strongly Taken (11) | Weakly Taken (10)
Weakly Taken (10) | Taken | Strongly Taken (11) | Weakly Not Taken (01)
Weakly Not Taken (01) | Not Taken | Weakly Taken (10) | Strongly Not Taken (00)
Strongly Not Taken (00) | Not Taken | Weakly Not Taken (01) | Strongly Not Taken (00)

## Slide 11
Section 3
Parallelism — Flynn's Taxonomy & ILP
11

## Slide 12
Flynn's Taxonomy
SENG 21213 · Computer Architecture & Operating Systems
12
Class | Instruction Streams | Data Streams | Description | Example
SISD | 1 | 1 | Classic sequential CPU — one instruction on one datum per cycle | Single-core (pre-1990)
SIMD | 1 | Many | One instruction applied to MULTIPLE data simultaneously — vector/array processing | GPU, x86 SSE/AVX, ARM NEON
MISD | Many | 1 | Multiple instructions, one data stream — mostly theoretical | Fault-tolerant aerospace systems
MIMD | Many | Many | Most general — multiple processors, independent instruction+data streams | SMP, multicore, cloud clusters

## Slide 13
ILP Techniques
SENG 21213 · Computer Architecture & Operating Systems
13
Technique | Description | Hardware Complexity
Superscalar | Issue 2+ independent instructions per cycle to replicated functional units | Medium — detect independence at runtime
Out-of-order (OOO) | Execute instructions out of program order when data deps allow; commit in order | High — reservation stations, ROB, register renaming
VLIW | Compiler packs multiple independent ops into one wide instruction | Low hardware; high compiler complexity — brittle
Speculative Execution | Execute instructions before knowing if needed (after branch); discard if wrong | High — branch predictor + rollback logic
SMT (HyperThreading) | One physical core appears as 2+ logical CPUs; hides memory latency by running threads | Medium — shared FUs, separate register files

## Slide 14
Practice Exercise
SENG 21213 · Computer Architecture & Operating Systems
14
✎ Exercise 6.1 — Pipeline Hazard Analysis [12 marks]
5-stage pipeline @ 1 GHz. 10-instruction sequence: 2 RAW hazards (2-cycle stalls each, no forwarding); 1 branch flush (3 cycles).
(a) [4] Calculate total cycles and effective CPI.
(b) [4] With forwarding: RAW stalls → 0 cycles. Branch flush remains 3 cycles. New CPI? Speedup from forwarding?
(c) [4] A loop of 8 instructions runs 1000 iterations. Branch always taken except last. Starting state: Strongly Not Taken. Trace first 3 iterations. Total mispredictions and penalty cycles?

## Slide 15
Key Takeaways
Pipelining, Branch Prediction & Parallelism
5-stage pipeline: IF→ID→EX→MEM→WB; ideal CPI=1; speedup ≈ k for large N
Structural: split I-cache/D-cache. Data RAW: forwarding eliminates most stalls. Control: branch prediction
Load-use hazard: 1-cycle stall unavoidable with forwarding — compiler fills with independent instr
2-bit predictor: 4 states; stable on loops; ~90% accuracy — standard in most real CPUs
Flynn: SISD (sequential) SIMD (GPU/vector) MISD (rare) MIMD (multicore/SMP)
ILP: superscalar, OOO execution, VLIW, speculation, SMT — all hide latency and increase throughput
15