## Slide 1
Lecture 07
Assembly Language & HW/SW Integration
x86 Registers · Instructions · cdecl Convention · Stack Frames · Boot Sequence
SENG 21213 · Computer Architecture & Operating Systems
1

## Slide 2
Learning Objectives
SENG 21213 · Computer Architecture & Operating Systems
2
By the end of this lecture you should be able to:
1. Identify all x86-32 general-purpose registers and their sub-registers and primary uses
2. Write x86-32 NASM assembly using data movement, arithmetic, logic, and control flow instructions
3. Trace the complete cdecl calling convention through 8 steps including stack frame layout
4. Draw a stack frame diagram showing saved EBP, return address, arguments, and local variables
5. Describe the 10-step boot sequence from CPU reset to kernel_main() execution
6. Explain Real Mode, Protected Mode, and Long Mode and the CR0 bit 0 transition mechanism

## Slide 3
Section 1
x86-32 Register Set
3

## Slide 4
x86-32 General-Purpose Registers
SENG 21213 · Computer Architecture & Operating Systems
4
Register | Size | Primary Use | Sub-registers
EAX | 32-bit | Accumulator; function return value; arithmetic | AX(16-bit), AH(8 high), AL(8 low)
EBX | 32-bit | Base pointer for data; callee-saved | BX, BH, BL
ECX | 32-bit | Loop counter (REP prefix); shift/rotate count | CX, CH, CL
EDX | 32-bit | Data; high word of MUL/DIV; I/O port address | DX, DH, DL
ESI | 32-bit | Source index for string ops (MOVS, CMPS) | SI (16-bit)
EDI | 32-bit | Destination index for string ops | DI (16-bit)
ESP | 32-bit | Stack Pointer — points to TOP of stack (decrements downward!) | SP (16-bit)
EBP | 32-bit | Base Pointer — anchor of current stack frame | BP (16-bit)
EFLAGS | 32-bit | CF(carry), ZF(zero), SF(sign), OF(overflow), IF(interrupt enable) | individual bits

## Slide 5
Section 2
Stack and Calling Convention
5

## Slide 6
Stack Operations — x86 Grows DOWNWARD
SENG 21213 · Computer Architecture & Operating Systems
6
Instruction | Pseudo-Code | ESP Change
PUSH src | ESP ← ESP − 4; Memory[ESP] ← src | Decreases by 4 (stack grows down)
POP dst | dst ← Memory[ESP]; ESP ← ESP + 4 | Increases by 4
CALL addr | PUSH EIP; JMP addr | ESP decreases by 4 (saves return address)
RET | POP EIP | ESP increases by 4 (restores return address)
SUB ESP, n | Allocates n bytes for local variables | ESP decreases by n

## Slide 7
cdecl Calling Convention — 8 Steps
SENG 21213 · Computer Architecture & Operating Systems
7
1. Caller PUSHes arguments RIGHT-TO-LEFT: PUSH arg3; PUSH arg2; PUSH arg1
2. Caller: CALL func — PUSHes return address (EIP); JMPs to func
3. Callee prologue: PUSH EBP; MOV EBP, ESP (save and set frame pointer)
4. Callee allocates locals: SUB ESP, n (n = total bytes for local vars)
5. Access args via positive EBP offsets: [EBP+8]=arg1, [EBP+12]=arg2…
6. Access locals via negative offsets: [EBP−4]=local1, [EBP−8]=local2…
7. Return value in EAX (32-bit) or EDX:EAX (64-bit value)
8. Callee: LEAVE (or MOV ESP,EBP; POP EBP); RET. Caller: ADD ESP, n×4

## Slide 8
cdecl Stack Frame — int add(int a, int b)
SENG 21213 · Computer Architecture & Operating Systems
8
ASM
add:
push ebp ; save caller's frame pointer
mov ebp, esp ; EBP = frame anchor for this function
; Stack layout:
; [EBP + 0] = saved EBP (just pushed)
; [EBP + 4] = return address (pushed by CALL)
; [EBP + 8] = argument a (first arg, pushed last)
; [EBP + 12] = argument b (second arg, pushed first)
mov eax, [ebp + 8] ; EAX = a
add eax, [ebp + 12] ; EAX = a + b ← return value in EAX
pop ebp ; restore caller's frame pointer
ret ; return (cdecl: caller does ADD ESP, 8)

## Slide 9
Section 3
Boot Sequence & CPU Modes
9

## Slide 10
x86 CPU Modes
SENG 21213 · Computer Architecture & Operating Systems
10
Mode | Addressing | Memory Limit | Protection | Usage
Real Mode | Segment:Offset (20-bit physical) | 1 MB (2²⁰ bytes) | None — all code has full access | BIOS POST; bootloader stage 1; SENG OS boot.asm starts here
Protected Mode (32-bit) | 32-bit virtual via GDT/LDT + paging | 4 GB (2³²) | Ring 0–3; segmentation + paging | 32-bit kernels; your Stage 0 kernel runs here
Long Mode (64-bit) | 64-bit virtual; paging required | 128 TB virtual | Ring 0 & 3; paging mandatory | Modern 64-bit OS (Linux, Windows 10+)

## Slide 11
Boot Sequence — CPU Reset to kernel_main()
SENG 21213 · Computer Architecture & Operating Systems
11
1. Power-on: CPU reset vector = 0xFFFFFFF0; executes BIOS/UEFI from ROM
2. POST: BIOS tests CPU, memory, I/O controller; initialises hardware
3. BIOS finds boot device; loads MBR (512 bytes) to 0x7C00 in Real Mode RAM
4. boot.asm at 0x7C00: loads 64 disk sectors using INT 0x13 extended read
5. Bootloader sets up 3-entry GDT: null, code segment (Ring 0), data segment
6. Set CR0 bit 0 = 1 → CPU switches from Real Mode to Protected Mode
7. FAR JUMP: reloads CS with code segment selector; flushes pipeline
8. Load DS/ES/SS = data segment selector; set ESP = 0x90000 (kernel stack top)
9. call kernel_main() — OS is now in charge; shell loop begins

## Slide 12
Why FAR JUMP After CR0?
SENG 21213 · Computer Architecture & Operating Systems
12
⚠ Critical: Pipeline Flush Required After Mode Switch
When CR0 bit 0 is set, the CPU mode changes immediately in hardware
BUT the instruction pipeline still contains Real Mode instruction bytes already fetched
Those pre-fetched bytes would be decoded as 16-bit Real Mode instructions — WRONG
The FAR JUMP flushes the entire instruction pipeline AND reloads CS with the new 32-bit code segment selector
Without the far jump: CPU would execute garbled instructions from stale pipeline — immediate crash
This is why boot.asm uses: jmp 0x08:protected_mode_entry — cannot use near jump here

## Slide 13
Practice Exercise
SENG 21213 · Computer Architecture & Operating Systems
13
✎ Exercise 7.1 — Stack Frame Trace [14 marks]
C function: int calc(int x, int y, int z) { int tmp = x+y; return tmp*z; } called with (3, 5, 7)
(a) [6] Show all PUSH instructions caller executes. Draw stack layout at function start (each cell: address relative to EBP, value). Show assembly for function body.
(b) [4] A 16-byte buffer buf[] is vulnerable: void vuln() { char buf[16]; gets(buf); }. Input is 20 A's + 4 bytes 0xCD 0xAB 0x04 0x08. What cell is overwritten? What happens on RET?
(c) [4] Why must a FAR JUMP immediately follow setting CR0 bit 0? What would happen without it? Which register is reloaded?

## Slide 14
Key Takeaways
Assembly Language & HW/SW Integration
x86-32 registers: EAX(return), ECX(count), ESP(stack top), EBP(frame base), EFLAGS
Stack grows DOWNWARD — PUSH decrements ESP; POP increments ESP
cdecl: args pushed right-to-left; callee saves EBP; args at [EBP+8+]; locals at [EBP-n]
Return value always in EAX; caller responsible for cleaning up argument stack space
Boot: BIOS → MBR (Real Mode 0x7C00) → GDT setup → CR0 bit0=1 → FAR JMP → kernel
FAR JMP is mandatory: flushes pipeline AND reloads CS with 32-bit code segment selector
14